## Slide 1: Final Year Project Lego Robot Guided by Wi-Fi (QYA2)
Presented by: Li Chun Kit (Ash)
So Hung Wai (Rex)

## Slide 2: Overview
Introduction
Video Demo
System Functions - Localization - Self-Guiding - Obstacles Detection - Auto Data Collection
Conclusion
Q&A

## Slide 3: Introduction
Goals
Wi-Fi Indoor localization
Self-Guiding
Lego robot as the media
to move and collect data
automatically
Figure 1. The client-server architecture.

## Slide 4: Video Demo

## Slide 5: Localization
Offline Phrase | Online Phrase
Data collected for establishing the training database | Observed data is compared with the training database
Estimated Location
Machine Learning Algorithm
Figure 2. Records in training database.
Figure 3. Observed data received during online phrase.

## Slide 6: Localization : K-Nearest Neighbor (KNN)
K=10
K=4
Classification by computing similarity between observed data and records in training database.
For each record in database :
Euclidean Distance
b
a
c
Records in grid a, band c
Figure 4. For k=4, the user trace is classified to be grid c record; while it is classified to be grid a when k=10.
The grid cell having the highest occurrence in the first k most similar records is the estimated location.

## Slide 7: Localization: Bayesian Probability
Chart: a RSSI Profile
| -80 | -78 | -76 | -74 | -72 | -70 | -68 | -66 | -64 | -62 | -60 | -58
A RSSI Profile | 0 | 0 | 0.04 | 0.03 | 0.05 | 0.15 | 0.22 | 0.25 | 0.2 | 0.06 | 0 | 0
Bayesian approach is based on signal strength distribution on each grid cell.
mitigates the random errors
adopts probability measurements
Figure 5. A histogram showing the RSSI distribution of an access point at a grid cell
computes across 106 grid cells

## Slide 8: Intuitively
Chart: RSSI Profile of 00:17:DF:AA:9B:A2 at Grid 82
| -68 | -65 | -62 | -59 | -56 | -53 | -50 | -47 | -44 | -41 | -38 | -35
A RSSI Profile | 0 | 0 | 0.04 | 0.03 | 0.05 | 0.15 | 0.22 | 0.25 | 0.2 | 0.06 | 0 | 0
Figure 2. Records in training database.
Bayesian Probability

## Slide 9: In Practice
Mac Address |  | RSSI probability |  |  |  | 
 |  | -60 | -58 | -56 | -54 | ……
 | 00:17:DF:AA:9B:A2 | 0.00 | 0.00 | 0.02 | 0.10 | ……
 | 00:23:EB:0B:4F:F5 | 0.02 | 0.11 | 0.25 | 0.20 | ……
 | 00:23:EB:0B:51:55 | 0.01 | 0.23 | 0.18 | 0.02 | ……
 | …… | …… | …… | …… | …… | ……
Grid Cell 82
RSSI Profiles
Mac Address |  | RSSI probability |  |  |  | 
 |  | -60 | -58 | -56 | -54 | ……
 | 00:23:EB:0B:4F:F5 | 0.20 | 0.24 | 0.10 | 0.03 | ……
 | 00:23:EB:3A:12:20 | 0.00 | 0.00 | 0.05 | 0.08 | ……
 | 00:17:DF:AA:9E:C1 | 0.01 | 0.02 | 0.13 | 0.18 | ……
 | …… | …… | …… | …… | …… | ……
Grid Cell 83
RSSI Profiles
Bayesian Probability

## Slide 10: Algorithm Accuracy
Chart: Accuracy of Localization
| 0 | 5 | 10
KNN | 0.076923 | 0.55769 | 0.73077
Baye | 0.36538 | 0.82692 | 1

## Slide 11: Appendix
KNN Demonstration

## Slide 12: Appendix
Bayesian Formula

## Slide 13: Appendix